# Supplier Quality Manual

## Working together as a team

### “QUALITY AT THE SOURCE”

Supplier Quality Manual

Edition: Revision 08, May 14, 2023

This document is controlled by:

JVIS-USA LLC

It is the user's responsibility to assure that only the latest revision of this standard is used.

The latest revision can be obtained online at:

www.jvis.us

Table of Contents

1.0	Introduction

2.0	Definitions

3.0	Documentation

3.1	General

3.2	JVIS Specific Documentation

3.3	Reference Documents

3.4	Original Equipment Manufacturer (OEM) Customer Requirements

3.5	US Legal Requirements

3.5.1	Conflict Mineral Disclosure

3.5.2	US Economic Sanctions

4.0	JVIS / Supplier Interface

4.1	General

4.2	Communication

4.3	Product Verification

5.0	Supplier Pre-Selection Phase

5.1	Supplier Assessment

6.0	Supplier Selection

7.0	Advanced Product Quality Planning (APQP)

7.1	General

7.2	Project Management Timeline

  - Non - Production Trail Sample Material

7.4	Special Characteristics

7.5	Control of Designated Characteristics

7.6	Safety Items

8.0	JVIS PA and PDR Process

8.1	General

9.0	Production Part Approval Process (PPAP)

9.1	General

    - Submission Levels Requirements

    - Material Sample Quantity

    - Statistical Data

    - Measurement Results Correlation

    - Packaging and Labeling Requirements

    - IMDS Submission

9.3	Identification

9.4       First Production Shipment Authorization

9.5       Annual PPAP Re-Certification

10.0	Audits/Supplier Assessment

10.1	Audit Conditions

  - Audit Criteria

10.3 	Special Process Assessments - Heat Treating, Plating & Coatings

10.3.1 Heat Treating Processes

10.3.2 Plating Processes

10.3.3 Coating Processes

10.3.4 Welding Processes

10.3.5 Molding Processes

11.0	Quality Data Submissions

12.0	Specification / Requirement Change / Concession Requests

12.1	General

12.2	Concessions

12.3	Permanent Changes

12.3.1	Supplier Request for Engineering Approval (S.R.E.A.)

12.3.2	JVIS Initiated Engineering Changes

12.3.3	General Change Requirements

13.0	Non-Conformance, Corrective and Preventive Actions

13.1     Requirements

13.1.1 Initial Containment

13.1.2 Certified Shipments

13.1.3 Initial Response

13.1.4 Formal Corrective Action

13.1.5 Supplier Containment Level Procedures

14.0	Supplier Quality Performance

14.1	General

14.2	Criteria

14.3	Performance Results

14.4	Supplier Development

14.4.1 Prioritization

15.0     Statistical Techniques (SPC)

16.0	Analytical Techniques

17.0	Measurement Systems Analysis (MSA)

18.0	Error Proofing

19.0	Preventive / Predictive Maintenance

20.0	Continuous Improvement Process (CIP)

###### QUALITY REQUIREMENTS FOR SUPPLIERS

1.0	INTRODUCTION

JVIS USA’s success is based upon the quality, performance, and economics of our products. The quality of our products depends on Zero Defects product purchased from our suppliers.  To assure the highest product quality possible, JVIS USA considers its suppliers as valuable team members.

Overview

Our commitment to steady, long-term improvement in our products and processes is the cornerstone of our business strategy. Maintaining customer satisfaction and enhancing shareholder value is a mutual goal of both JVIS USA and its suppliers. To achieve this objective, we must continuously work together to improve the overall efficiency and productivity of our engineering, manufacturing, administrative, and support organizations.

Quality Policy

JVIS USA’s Quality Policy is included in this standard and it is posted on our website and it is our wish that our suppliers share the same principals as we have committed to.

Quality System Requirements

Suppliers to JVIS USA must meet one of the following minimum quality system requirements:

- Third party registration to the latest version of ISO 9001 by an accredited third party certification body, unless otherwise specified by the customer

- Certification to the latest version of  ISO9001 with compliance to other customer defined Quality Management System requirements, such as MAQMSR (Minimum Automotive Quality Management System Requirements) (http://www.iatfglobaloversight.org/) through 2nd party audit.

- Certification to the latest version of ISO 9001 with compliance to the latest version of  IATF 16949 through 2nd party audits.

- Certification to the latest version of IATF 16949 through third party audits.

- “Exempt supplier” established by JVIS, wherein certain specified elements of the latest version of  ISO 9001 or IATF 16949 may be waived.  “Exempt” refers to $30,000 or less supplied to JVIS per Calendar year.

Copies of ISO 9001/ IATF 16949 / ISO 14001 registration certificates shall be submitted to the JVIS Sourcing Team. Should the status of any accepted accreditation change, (i.e. new certification, de-certification, reassessments, etc.) the supplier shall notify the JVIS Sourcing Team.

Purpose:

This Standard is a supplement providing additional JVIS specific requirements, which suppliers shall follow. This supplement, with the the latest version of IATF 16949 Technical Specification, includes both supplier and JVIS responsibilities.  Material supplied to JVIS shall be produced, controlled, inspected, and tested according to the requirements set forth in these documents and other applicable specifications.

2.0	DEFINITIONS

      - The word ‘shall’ indicates a mandatory requirement.

-	The word ‘should’ indicates a mandatory requirement with some flexibility allowed in compliance methodology.  Suppliers choosing other approaches to satisfy a 'should' must be able to show that their approach meets the intent of the latest version of  IATF 16949.

-	'Product’ is defined as any part, product, service, etc. supplied to JVIS for which this standard is applicable.

When referring to this Standard and the latest version of IATF 16949 Technical Specification in the development and assessment of Suppliers to JVIS, the following applies:

-	Customer			=	JVIS

-	Supplier 			=		External Provider to JVIS - the type and extent of control applied to the supplier and the purchased product/service shall be dependent upon the effect of the purchased product/service on subsequent product realization of the final JVIS product.

-	JVIS Sourcing Team	=		Team of JVIS associates representing JVIS specific departments

3.0	DOCUMENTATION

3.1	GENERAL

The supplier shall maintain and conform to the latest revision level of the required or referenced Purchase Order documentation.

3.2	JVIS SPECIFIC DOCUMENTATION

JVIS USA specific documentation related to Product conformance may include, but is not limited to the following:

-	Parts list, Product structure (bill of materials)

-	Blueprints and or data

-	Order specifications

-	Other supporting specifications/documentation

3.3	REFERENCE DOCUMENTS

The following is a list of AIAG/ISO/ANSI documents referenced in this standard:

| Manual | Published by | Description |
| --- | --- | --- |
| IATF 16949 | IATF | Technical Specification |
| ISO 9001 | ISO | Quality System |
| AIAG CQI-19 | AIAG | Subtier Supplier Management Process Guideline |
| AIAG CQI-9 | AIAG | Heat Treat System Assessment |
| AIAG CQI-11 | AIAG | Plating System Assessment |
| AIAG CQI-12 | AIAG | Coating System Assessment |
| AIAG CQI-15 | AIAG | Welding Table |
| AIAG CQI-23 | AIAG | Molding Assessment |
| FCA CSR | IATF | FCA Customer Specific Requirements |
| GM CSR | IATF | GM Customer Specific Requirements |
| APQP | AIAG | Advance Product Quality Planning & Control Plan |
| FMEA | AIAG | Potential Failure Mode and Effects Analysis |
| MSA | AIAG | Measurement System Analysis |
| SPC | AIAG | Fundamental SPC |
| PPAP | AIAG | Production Part Approval Process |
| ANSI Y 14.5 | ANSI | GD&T |
| MAQMSR (Minimum Automotive Quality Management System Requirements |
| REFER TO THE LATEST VERSION |

To obtain information of these documents above, contact the following:

http://www.aiag.org/

http://www.iso.org/

http://www.ansi.org/

http://www.iatfglobaloversight.org/

  - ORIGINAL EQUIPMENT MANUFACTURER (OEM) CUSTOMER

REQUIREMENTS

The supplier shall adhere to referenced OEM Customer requirements as communicated per JVIS USA documentation.  Also refer to: http://www.iaob.org/ for an outline of OEM Customer requirements.

The supplier shall adhere to all statutory and regulatory requirements in the country of receipt, the country of shipment and the customer identified country of destination if provided.

The supplier, in turn, shall cascade JVIS USA and applicable OEM requirements to their suppliers.

  - US LEGAL REQUIREMENTS

The supplier shall adhere to the applicable legal requirements, but is not limited to the following:

3.5.1 	CONFLICT MINERALS DISCLOSURE

The minerals TIN, TANTALUM, TUNGSTEN and GOLD (also referred to as “3TG”) are considered “conflict minerals”.  The Dodd-Frank Act requires conflict minerals disclosure to discourage companies from engaging in trade which may support human rights abuse and funding of illegal armed groups in the Democratic Republic of Congo (DRC) and the surrounding countries - Angola, Burundi, Central African Republic, Republic of the Congo, Rwanda, South Sudan, Tanzania, Uganda, and Zambia.

The Securities Exchange Commission (SEC) published final rules associated with the disclosure of the source of conflict minerals. (See the rules at www.sec.gov).

The latest Conflict Minerals Reporting Template (CMRT) and information can be found on the Responsible Minerals Initiative website (www.responsiblemineralsinitiative.org).

The supplier shall submit a CMRT annually to the appropriate JVIS Conflict Minerals Representative.

3.5.2 	U.S. ECONOMIC SANCTIONS

JVIS USA takes its responsibility to comply with the applicable U.S. Economic Sanctions seriously and makes every effort to comply and expects that the supplier also comply to the applicable U.S Economic Sanctions.

Current U.S. Economic Sanctions information, the Specially Designated Nationals and Blocked Persons lists (SDN List), and other lists published by the Office of Foreign Assets Control (OFAC) can be found on the U.S. Department of the Treasury’s website www.treasury.gov

4.0	JVIS / SUPPLIER INTERFACE

4.1	GENERAL

The supplier shall communicate through the JVIS USA Buyer unless otherwise specified. The official business language for all documents referenced in this quality standard shall be English.

Other languages may be used with prior JVIS approval.

Note: The supplier shall communicate any management or ownership changes to the JVIS buyer immediately.

4.2	COMMUNICATION

Communication is the key to any successful partnership.  JVIS USA involves the supplier from product concept through mass production.

4.3	PRODUCT VERIFICATION

JVIS and its customers shall be afforded the right to verify the supplier’s products, processes and systems at JVIS USA or supplier’s location(s).

5.0	SUPPLIER PRE-SELECTION

5.1	SUPPLIER ASSESSMENT

Potential suppliers may be requested to complete a JVIS Supplier Quality Risk Assessment which could be used in the planning of an on-site assessment.

JVIS may choose to conduct an on-site assessment (Reference JVIS SQA Survey CORP-TPC-073) of one or more potential suppliers before selecting a source due to current performance issues with an existing supplier or to better understand the capability of a potential new supplier.

6.0	SUPPLIER SELECTION

Upon review of gathered information on each potential supplier by the JVIS Sourcing Team, a decision will be made and the business will be awarded.

7.0	ADVANCED PRODUCT QUALITY PLANNING (APQP)

7.1	GENERAL

The supplier shall utilize the planning procedures from the AIAG Advanced Quality Planning and Control Plan (APQP) manual.  All elements of the APQP must be incorporated into the planning process, unless waived in writing by the JVIS Sourcing Team.  All documents including Process Flow Diagram, PFMEA and Process Control Plans shall include all processes for the manufacturing of components, including incoming inspection, internal transportation, secondary operations, outside services and packaging.

All operations shall be keyed to the Process Flow Diagram, PFMEA and Process Control Plan.

7.2.	PROJECT MANAGEMENT TIMELINE

The supplier shall develop a Project Management Timeline, which contains (at minimum) program events, target dates and assigned responsibilities.  The purpose of the Timeline is to assure the timing of programs as defined by the JVIS Sourcing Team.

The Timeline shall be maintained at the supplier at all times.  Updated copies shall be submitted to the JVIS Sourcing Team if requested.

7.3	NON - PRODUCTION SAMPLE MATERIAL

Non - production trial sample (i.e. prototype, R&D samples etc.) shipments shall be identified with the appropriate label and shipped separately from production intent material.

7.4	SPECIAL CHARACTERISTICS

'Special Characteristics' are selected by JVIS USA with the supplier through knowledge of product and process and are identified by 'SC' and/or customer specific symbols on the drawing, in the specification or other supplemental documentation.   The presence of the 'Special Characteristics' is not intended to reduce the importance of other dimensions and /or characteristics selected by the supplier.  They shall be included on the PFMEA, Process Control Plan and process instructions unless otherwise agreed upon by the JVIS Sourcing team.

7.5 	CONTROL OF DESIGNATED CHARACTERISTICS

Items specified as 'Special Characteristics' require manufacturing control to assure compliance. The control data shall be documented and retained at the supplier’s facility and shall be available for submission and/or review by the JVIS USA Supplier Quality Engineer.

Unless otherwise specified, refer to the latest version of the AIAG PPAP manual for capability levels on designated characteristics at time of PPAP and serial production.

7.6	SAFETY ITEMS

JVIS USA and its customers identify Safety items on the blueprints and  or data utilizing symbols such as an inverted delta     (Ford), a <S> (FCA safety) or <D> (FCA dimensional), or other industry recognized symbols.

8.0	JVIS PA & PDR

8.1	GENERAL

The JVIS USA PA (Process Audit) and PDR (Production Demonstration Run) is conducted for all parts determined by the customer to be HIGH RISK to the vehicle program.

If any non-acceptances are noted, then the PA and PDR remains open. Corresponding corrective action shall be submitted by the supplier and validated through a re-visit and/or re-evaluation by the Sourcing Team for PA and PDR closure.

Note:

Once a PA and PDR have been approved, changes to the supplier's production process cannot be implemented without prior JVIS Sourcing Team approval.  The SREA (Supplier Request for Engineering Approval Form shall be submitted for approval to the JVIS Sourcing Team, if the supplier wants to implement process changes.

9.0      PRODUCTION PART APPROVAL PROCESS (PPAP)

9.1	GENERAL

The supplier shall submit a PPAP in accordance with the latest revision of the AIAG PRODUCTION PART APPROVAL PROCESS (PPAP) manual unless otherwise specified by the JVIS USA Supplier Quality.

9.2	SUBMISSION LEVEL REQUIREMENTS

The supplier must complete all of the applicable PPAP requirements as stated in the latest revision of the AIAG PPAP Manual, regardless of the level of submission requested (CQI-19). For example, if a level 1 submission is requested, it is expected that the supplier will have completed the rest of PPAP requirements and have the records available on-site.

The submission level is a level 3 as the default for all submissions unless specified otherwise by JVIS USA Supplier Quality.

JVIS USA specific requirements related to the PPAP include the following:

9.2.1		MATERIAL SAMPLE QUANTITY

Standard sample quantity for dimensional evaluation shall be six (6) product (per cavity, die, progressive die, etc. if applicable) unless otherwise specified.

9.2.2		STATISTICAL DATA

Supporting statistical data (i.e. SPC, process capability studies, etc.) for a

PPAP submission should be done using product from the PDR or from a 'significant material production run'; as defined per the AIAG standard as whichever is more, 300 pieces or 2 hours of production.

9.2.3		MEASUREMENT RESULTS CORRELATION

All samples shall be sequentially numbered and correlated to the dimensional reports.  Blueprints should be numbered in accordance with the latest revision of ANSI Y 14.5 standards.  All results shall be taken from master samples and these samples shall be submitted with the PPAP. Measurement method agreement, if defined, shall be attached to the supplier dimensional evaluation report.

9.2.4      PACKAGING AND LABELING REQUIREMENTS

The supplier is responsible to assure the packaging used protects the product from damage during shipment to JVIS USA. Failure to conform to this requirement could result in a PA or PPAP rejection. JVIS USA requires two (2) container labels per container. The responsibility for ensuring component quality from your plant to the point of use remains with you - the supplier of the product.

9.2.5      IMDS SUBMISSION

No PPAP will be fully approved by JVIS USA without acceptance and         verification of IMDS approval (Industrial Material Data System http://mdsystem.com/).

Supplier PPAP packages must contain a copy of the acceptance screenshot from the IMDS.

Note:	Before any PPAP submission, deviations from these requirements shall be agreed upon between the supplier and the JVIS Sourcing Team.

9.3	IDENTIFICATION

All samples accompanying PPAP submissions shall be identified with the appropriate label on the carton or container.  The label shall contain all required information and shipped separately from production material.

9.4	FIRST PRODUCTION SHIPMENT AUTHORIZATION

The supplier shall ship production intent material to JVIS USA only if:

1.	The PPAP submission has been approved in writing by the JVIS USA Supplier Quality Representative and the supplier has received written notification of the approval.

Note:	The supplier shall not ship production intent material without prior PPAP approval by the JVIS USA Supplier Quality Representative.

9.5	ANNUAL PPAP RE-CERTIFICATION

An annual material re-certification (once per calendar year) of the supplied material shall be performed by the supplier unless otherwise specified by the JVIS Sourcing team.  Questions regarding the re-certification should be directed to the respective JVIS USA Supplier Quality Representative.  The results of the re-certification shall be documented and maintained at the Supplier’s site. These shall be available upon request.

10.0	AUDITS/SUPPLIER ASSESSMENTS

10.1	AUDIT CONDITIONS

Conditions, which could warrant 2nd party audits include the following as a

minimum:

-     Supplier Approval (not ISO 9001 certified)

-     Supplier Risk Assessment results in Medium or High Risk.

-     Supplier Monitoring (Quality/Delivery performance)

-     Supplier QMS Development

-     Product Audits

-     Engineering changes

-     Process changes

-     Plant location changes (e.g. Tool transfer) which also requires	a new PA and PDR and PPAP submission.

10.2	AUDIT CRITERIA

The criteria for these audits focus on certification, performance, product and process changes. However, other criteria may be utilized.   The JVIS USA Supplier Quality Representative shall determine the appropriate criteria and communicate this information to the supplier’s Quality/Sales Department.

  - Special Process Assessments

Suppliers supplying the services of heat treating, plating, welding, molding and/or coatings shall meet the following requirements:

    - Heat Treating Processes

Applicability and effectiveness of heat treating processes shall be determined utilizing CQI-9 Special Process: Heat Treat System Assessment published by the AIAG. The effectiveness evaluation shall include the organization’s self-assessment, actions taken, and that records are maintained.

    - Plating Processes

Applicability and effectiveness of plating processes shall be determined utilizing CQI-11 Special Process: Plating System Assessment published by the AIAG and available at www.AIAG.org. The effectiveness evaluation shall include the organization’s self assessment, actions taken, and that records are maintained.

    - Coating Processes

Applicability and effectiveness of coating processes shall be determined utilizing CQI-12 Special Process: Coating System Assessment published by the AIAG and available at www.AIAG.org. The effectiveness evaluation shall include the organization’s self assessment, actions taken, and that records are maintained.

    - Welding Processes

Applicability and effectiveness of welding processes shall be determined utilizing CQI-15 Special Process: Welding Table published by the AIAG and available at www.AIAG.org. The effectiveness evaluation shall include the organization’s self-assessment, actions taken, and that records are maintained

    - Molding Processes

Applicability and effectiveness of molding processes shall be determined utilizing CQI-23 Special Process: Molding System Assessment published by the AIAG and available at www.AIAG.org. The effectiveness evaluation shall include the organization’s self-assessment, actions taken, and that records are maintained

11.0	QUALITY DATA SUBMISSIONS

The supplier may be required to submit Quality Data (i.e. SPC charts, process monitoring results, material certifications, preventative & predictive maintenance data, etc.)  upon request, to the JVIS Sourcing Team. Original documentation shall be retained at the supplier.

12.0	SPECIFICATION / REQUIREMENT CHANGE / CONCESSION REQUESTS

12.1	GENERAL

Requests for changes or concessions (temporary or permanent) to specifications or requirements shall be documented in writing and approval shall (must) be made through the JVIS Sourcing Team.

12.2	CONCESSIONS

Concessions are time or quantity limited deviations from specifications.  These concessions shall be temporary and are not considered permanent. All concession parts are to be labeled with a description of the concession.  Prior to shipment, supplier must notify the responsible Supplier Quality Engineer (SQE) of concession shipment.

12.3	PERMANENT CHANGES

Permanent changes, either Supplier or JVIS USA initiated, shall be appropriately documented. These changes shall require a new PPAP submission as specified by JVIS Sourcing Team (if not specified, submissions shall default to the Level 3).

12.3.1	SUPPLIER REQUEST FOR ENGINEERING APPROVAL (S.R.E.A.)

Supplier initiated change requests shall be submitted to JVIS USA utilizing the JVIS USA S.R.E.A. form. This form and all supporting documentation shall be submitted to the JVIS USA Purchasing Department.  Please contact JVIS USA Purchasing or Supplier Quality for a copy of this form.

The supplier shall make no changes until JVIS USA approval has been granted.

12.3.2	JVIS USA INITIATED ENGINEERING CHANGES

JVIS USA initiated engineering changes, including all PPAP requirements, shall be communicated to the supplier by the JVIS Sourcing Team.

12.3.3	GENERAL CHANGE REQUIREMENTS

General changes (i.e. flow charts, control charts, etc.) shall be requested through the applicable JVIS Sourcing Team Representative.

Note:	No change to material shall be implemented until all proper authorization has been obtained. This includes PPAP submission requirements as specified by the appropriate JVIS USA Supplier Quality Representative.

13.0	NONCONFORMANCE, CORRECTIVE AND PREVENTIVE ACTIONS

13.1	REQUIREMENTS

When JVIS USA has notified the supplier of a 'Nonconformance' issue with material, the supplier is responsible for the following (not including line accums);

13.1.1	 Initial Containment

This containment action shall be:

- Implemented within 24 hours (1 calendar day including weekends and holidays) of notification by JVIS USA personnel. (All verbal notifications by JVIS USA shall be followed up with written documentation).

- Containment actions shall include all affected material in the supplier's control, in transit to JVIS USA, in the possession of JVIS USA or finished product shipped to JVIS USA customers.

- The supplier shall notify JVIS USA Materials and Supplier Quality of certified material availability.

- The supplier shall notify the Supplier Quality Representative of their containment actions and to discuss coordination of containment of material at JVIS USA and JVIS USA  customers.

13.1.2	 Certified Shipments

All shipments of affected material shall be 'certified' (i.e. in compliance with the containment actions) until corrective action issues are formally closed by a JVIS USA Supplier Quality Representative.

All material shall be shipped per approved methods and identified with an 8.5” x 11” 100% certified product label on each container. JVIS USA may require individual component identification.

13.1.3	 Initial Response

A written initial response shall be submitted to the JVIS USA Quality Department within 24 hours (or otherwise specified time frame) of formal notification of the concern. This initial response shall, at minimum, contain:

-	JVIS Concern or DMR Number and Date of Nonconformance

-	Name of the JVIS Supplier Quality Representative

-	Problem Description

-	Containment action description

-	Containment action verification (quantitative results)

-	Certified material shipment dates and identification

-	Root Cause analysis status

-	Return Material Authorization (RMA) number must be given within 24 hours, otherwise the nonconforming material will be dispositioned/scrapped.

NOTE 1:	Each of the above stated criteria shall contain an implementation date and assigned responsibility.

NOTE 2:	If disposition has not been received within 24 hours JVIS USA LLC reserves the right to either sort, rework, scrap or return your rejected material.

13.1.4	 Formal Corrective Action Report

A Formal Corrective Action Report and supporting evidence shall be submitted to the JVIS USA Supplier Quality Department within 10 working days (or otherwise specified time frame) of formal notification of the concern. This formal written corrective action 8D report with implementation/effective dates and assigned responsibilities shall contain, at a minimum, the items listed below:

-     	Description of the concern and JVIS DMR/Concern Number

-	Containment action

-	Root Cause of the concern with verification

-	Corrective action

-		Verification of containment and corrective action.  This is a measure of the action's effectiveness utilizing appropriate statistical or process performance analysis methods.

-		Preventive measures for 'Lessons Learned' and applicable to similar products and processes.

-		Preventive actions assess the applicability of the action taken to similar processes.  These are actions with a proactive and predictive intention with the focus on avoiding occurrences.

-		FMEAs, Control Plans, Work Instructions and other appropriate documentation shall be revised to reflect changes resulting from the concern. These documents shall be maintained on file and provided to JVIS USA Supplier Quality Representative for review as required.

13.1.5	   Supplier Containment Level Procedures

If supplier containment actions are not effective, progressive JVIS USA initiated procedures shall be implemented for the supplier. The JVIS USA Supplier Quality Representative will define exit criteria. Any reoccurrence will result in the 30-day inspection period to start over. The inspection period begins once root cause has been identified and corrective actions are in place.

- Controlled shipping level 1 (CS1) - The supplier shall implement 100% inspection for a period not less that 30 days with no re-occurrence of the issue.

- Controlled shipping level 2 (CS2) - A containment process under customer control.  Containment conducted at customer site, supplier, or third-party location at the supplier’s expense.  This process may be used if Level 1 containment is ineffective at containing a nonconformance. The supplier shall implement 200% inspection for a period not less that 30 days with no re-occurrence of the issue.

14.0	SUPPLIER  QUALITY PERFORMANCE

14.1	GENERAL

The JVIS Sourcing Team, in regard to their ongoing quality and delivery performance, shall assess the supplier.

14.2	CRITERIA

Criteria for acceptable performance may include, but not limited to, the following:

- PPM (parts per million defective)

- DELIVERY (100% on time delivery)

- DMRs Occurrences

Scoring system (100 points per reporting period - quarterly)

  - Delivery = 40 points

    - 100% on time = 40 points

    - 99% to 95% = 30 points

    - 94% to 90% = 20 points

    - 89% to 85% = 10 points

    - 84% or below = 0 points

  - DMRs/Occurrences = 40 points

    - 0 DMRs = 40 points

    - 1 to 3 = 30 points

    - 4 to 6 = 20 points

    - 7 to 9 = 10 points

    - 10+ = 0 points

  - PPMs = 20 points

    - 0 PPMs = 20 points

    - 1 to 300 PPMs = 17.5 points

    - 301 to 500 PPMs = 15 points

    - 501 to 1500 = 10 points

    - 1501 to 3500 = 5 points

    - 3501 + = 0 points

*A JVIS USA production shut down for a supplier quality or delivery issue is an automatic 30-point deduction.

SUPPLIER STATUS EXPLANATION

Green:		Most recent scorecard is 50 points or higher.

Status:		Supplier is a preferred supplier for new business.

Yellow:	Most recent scorecard is below 50 points.

Status:	New Business hold.  Exceptions are possible if supplier is actively participating in monthly continuous improvement plans.

Red:	Most recent scorecard is below 20 points, or scorecard is below 50 points for 4 consecutive periods.

Status:		New business hold with monthly supplier development meetings required.

14.3	PERFORMANCE RESULTS

Results of the quality performance assessments shall be documented by the JVIS USA Purchasing & Supplier Quality Department and communicated to the supplier.

The results of the assessments shall be communicated by the supplier to their management.

14.4	SUPPLIER DEVELOPMENT

14.4.1 Prioritization

Supplier development activities shall be prioritized based on the following:

- Supplier performance report scores.

- 2nd party audit findings – Major Nonconformances

- 3rd party certification status – Decertification, Suspension

- Risk Assessment

15.0	STATISTICAL TECHNIQUES

The supplier shall monitor process performance utilizing the appropriate statistical techniques (i.e. First-time yield, SPC, etc.) in accordance with the AIAG Statistical Process Control manual.

Additional areas in which statistical techniques may be applied are as follows:

-    Predictive maintenance programs

-    Gage R&R studies

-    Defect analysis

-    Continual Improvement Processes

The results of the statistical techniques shall be documented and retained at the supplier's location. This information shall be made available upon request to the JVIS Sourcing Team.

16.0	ANALYTICAL TECHNIQUES

The supplier should utilize analytical techniques to improve their process capabilities and problem resolution.

Examples of analytical techniques are as follows:

- Design of Experiment (DOE)

- Theory of Constraints

- Benchmarking

- Hoshin Planning

- Shainin

The results of analytical techniques should be documented and retained at the supplier's location. This information shall be made available upon request to the JVIS Sourcing Team.

17.0     MEASUREMENT SYSTEM ANALYSIS (MSA)

The supplier shall perform measurement system analysis (frequency to be determined by the supplier) in accordance with the AIAG Measurement System (MSA) manual.  With approval by the JVIS USA Supplier Quality Representative, other analytical methods and acceptance criteria may be implemented.  Results of MSA analysis shall be documented and retained at the supplier's location.  This information shall be available upon request to the JVIS Sourcing Team.

18.0	ERROR PROOFING

The supplier shall utilize error proofing as applicable the latest version of IATF 16949 Quality Systems Requirements standard.  Results of error proofing shall be documented and retained at the supplier's location.  This information shall be made available upon request to the JVIS Sourcing Team.

19.0	PREVENTIVE / PREDICTIVE MAINTENANCE

The supplier shall implement a preventive / predictive maintenance program for process Machine/equipment. Statistical data should be assimilated and systems developed for the implementation of predictive maintenance programs.  The supplier shall document and maintain this program and it shall be available upon request to the JVIS Sourcing Team.

20.0	CONTINUAL IMPROVEMENT PROCESS (CIP)

The supplier shall implement continual improvement efforts throughout their entire organization.  Results of the Continual Improvement Process shall be documented and retained at the supplier's location.  This information shall be made available upon request to the JVIS Sourcing Team.

By signing below JVIS USA and the Supplier agree to the requirements and content of this Supplier Quality Manual.

Agreed by,								Agreed by,

_______________________						_______________________

JVIS USA, LLC							Supplier

Date:									Date: